## Slide 1: Auto Chasing Turtle
Hirotaka Niisato
Noritsuna Imamura

## Slide 2: Agenda
Summary
Part “Hardware”
  Need more power supply
  Nothing display
  Need more more power supply
Part “Software”
  Not Bitmap
  Calculate the course
  Calculate the distance

## Slide 3: Summary
This product is "Auto Chasing Turtle".
  By autonomous control, this robot recognizes people's face and approaches to the detected human.
  Rotate and look for the human who becomes a target.
  Detect the human with recognizing people's face by using RGB camera of Kinect.
  If it can detect the human, it calculates the course which it should follow. And It direction is changed.
  Calculate the distance to target by using Z(depth) camera of Kinect.
  Walk toward to target.
  2-5 are repeated until it becomes a suitable distance. And if losts target, returns to 1.
  The scene that it is working in real time can be seen by iPad.

## Slide 4: Movie
YouTube
  http://www.youtube.com/watch?v=8EgfAk5RBVo
Source Code & detail explanation
  http://www.siprop.org/ja/2.0/index.php?product%2FAutoChasingTurtle

## Slide 5: complete set parts
Robot
  KONDO Animal 01
    http://fswg.oesf.biz/
Controllers
  For servo
    RCB3
  For application
    Beagleboard-xM
      Linaro-Kernel
      Android(Embedded Master)
Sensors
  RGB camera
  Z(Depth) camera
    Kinect
Connect to outside
  Radio wave
    Wi-Fi router
  Viewer
    iPad
Power supply
    12V1A output
    10V1A output
    5V3A output

## Slide 6
OpenFrameworks x Kinect x Android
=
ofxDroidKinect

## Slide 7: About ofxDroidKinect

## Slide 8: About ofxDroidKinect
This is the Android Application Framework which runs on openFrameworks & uses Kinect.
  Download
    http://www.noritsuna.com/archives/2011/01/openframeworks_kinect_android.html
Using softwares
  openFrameworks for Android
    It’s the gaming framework. You can make game easier.
      http://openframeworks.cc/
  Android
    Linaro Android
      http://git.linaro.org/gitweb?p=people/jstultz/linux.git;a=summary

## Slide 9: Part “Hardware”

## Slide 10: Need more power supply

## Slide 11: Need more power supply
Don’t run beagleboard-xM by 5V/1A power supply.
  It needs 5V/2A.
  Standard USB battery has 5V/1A.
Create power supply by myself
  My battery has 12V/2A.
  My plan is to create convertor of 12V/2A ⇒ 5V/2A.
  Can’t get power IC…
  Using car’s cigarette adapter which convert to USB.
    12V・24V/2A ⇒ 5V/2A

## Slide 12: Nothing display
Can’t view camera’s image
  Using VNC viewer
    It needs Wi-Fi router.
    We attached Wi-Fi router on beagleboard-xM.

## Slide 13: Need more more power supply
Can’t get IP address from Wi-Fi router
  Wi-Fi router needs more “Power supply”.
    Wi-Fi router: 1A + beagleboard-xM: 2A = Total: 3A

## Slide 14: Part “Software”

## Slide 15: Not Bitmap
Standard RGB camera(BITMAP) format
  32bit(int)
    8bit(A), 8bit(R), 8bit(G), 8bit(B)
Kinect’s RGB camera format by libfreenect
  3 int
    32bit(R), 32bit(G), 32bit(B)
A
R
B
G
8bit
8bit
8bit
8bit
32bit(int)
R
G
B
32bit(int)
32bit(int)
32bit(int)

## Slide 16: Not Bitmap
However ・・・・・・ can’t detect Face.
  Must convert format BMP to JPEG…
Bitmap bitmap = Bitmap.createBitmap(w, h, Bitmap.Config.ARGB_8888);
byte[] pixels = OFAndroid.getImgPixels();
if (pixels != null) {
for (int i=0;i<w;i++) {
for (int j=0;j<h;j++){
int index = (j * w + i) * 3;
bitmap.setPixel(i, j,
Color.rgb(pixels[index++],
pixels[index++],
pixels[index]));
}
}
FileOutputStream fos = new FileOutputStream("/screenshot.jpg");
bitmap.compress(Bitmap.CompressFormat.JPEG, 100, fos);
fos.flush(); fos.close();

## Slide 17: Calculate the course
Calculate the course which it should follow.
It direction is changed.
FaceDetector detector = new FaceDetector(w, h, faces.length);
int numFaces = detector.findFaces(bitmap, faces);
if (pointX > 0 && pointX < w/4) {
DroidBot.getInstance().turnRight2(); // right position
} else if (pointX >= w/4 && pointX <= 3*w/4) {
; // center position
} else if (pointX > 3*w/4 && pointX <= w) {
DroidBot.getInstance().turnLeft2(); // left position
}

## Slide 18: Calculate the course

## Slide 19: Calculate the course
Using height.
  Change Kinect’s angle.
int angle = 30 - pointY*30/h;
if (angle > 0 && angle <= 30)
OFAndroid.setAngle(angle);

## Slide 20: Calculate the distance
Calculate the distance to target by using Z(depth) camera of Kinect.
  Range 0~65565
int dist = OFAndroid.getDistance(pointX, pointY);
if (dist < 100) DroidBot.getInstance().walkBack4();
else if (dist >= 100 && dist < 150) DroidBot.getInstance().walkToward4();
else if (dist >= 150 && dist < 200) DroidBot.getInstance().walkToward8();
else if (dist >= 200 && dist < 300) DroidBot.getInstance().walkToward16();
else if (dist >= 300) DroidBot.getInstance().walkToward32();

## Slide 21: MAKE:style
Hardware
  beagleboard-xM
  KONDO Animal
  Kinect
Software
  ofxDroidKinect
    Linaro Kernel
    Android(Embedded Master)
Do It Yourself ⇒Do It With Others!